CNN 学习笔记

不同神经网络的区别主要在于：
1）激活函数
2）误差计算方法
3）优化算法
导致训练方法不同。
相比于全连接神经网络，CNN思路改变：
1）局部连接
2）权值共享
3）下采样
效果：训练参数减少，数据可为高维。

1.网络架构：
INPUT → [[CONV]*n → POOL?]*m→ [FC]*k
CONV:卷积层（非数学意义卷积） ，POOL：池化层 ，FC：全连接层
n个卷积层叠加后可选择性再叠加一个池化层，重复此结构m次，再叠加k个叠加层。
说明：
1）若INPUT为三维数据，即神经元将为三维NODE_i,j,k，有宽度、高度、深度信息
2）滤波器的个数是超参数

2.各层的输出计算及训练：
卷积层：
1）输出计算：
用滤波器与单通道（位于某深度的一层）卷积计算（有点类似于用filter遍历image，)，遍历步幅可调整
步幅，滤波器大小，图像大小，共同决定卷积后结果的大小：（图像边长+补边-滤波器边长+1）/ 步幅 +1
每卷积一次，得到一个Feature_map ,同一卷积层，所有卷积计算完，Feature Maps 将归结于深度信息。
说明：
i) 局部连接的体现：filter内部记录权值信息，若filter 3*3 则upper_stream_nodes = 9 ,down_stream_nodes = 1
filter_size sets upper_nodes connected.
ii) weights shared : each nerve cell use the same weights to calc_output. Kinds of filter sets kinds of weights.

2)

POOLING LAYER:
 Ignore sample_nodes which are representative badly .
 To simplify params
 Types: Max Pooling / General Pooling / Overlapping Pooling / mean Pooling / etc.
1) output calculation ( e.g. Max Pooling):
find the max value in a n*n(*n) cell in Feature_Maps as the represent.

CNN TRAIN:
    ====back broadcasting algorithm:====
1.calculate forward output
2.calculate back error : partial derivative from Loss_Function to weighting_input_NetCell
3.calculate gradient of weights: Pd(E_d)/Pd(w_i,j) = output_in * error_j
4.update weight each layer after all layers calculation done
    =============================
 1.train in conv layer: